POWER 2.53 by PAVEL BREDER (c) 1981, 1982

The system requirements are:

1)   CP/M 1.4x, 2.xx, MP/M
2)   20K minimum
3)   8080, Z-80, 8085
4)   ORG normally 100H unless specified

?              show commands
LOG            show CP log information
DIR            list directory
COPY           copy file
USER  n        set USER (n=0 to 31) (sets XUSER)
XUSER n        set destination USER (n=0 to 31)
INFO           type this file
STAT           show free disk space
DISK           show disk information
GROUP	       show extent number(s) and groups used
TEST           test and checksum disk
RECLAIM        recover deleted file
EXIT           exit CP
TYPE           type file
TYPEH          type file in hex
TYPEA          type file in ascii
TYPEX          type file in hex and ascii
SIZE           show file size
CHECK          checksum file (16 bit CRC)
ERA            erase file
REN            rename file (wild cards OK; enter new name at prompt)
RUN            execute COM file (to use arguments, must use RUN filename)
SPEED n        set output speed of display (0-9 0=fast)
JP      xxxx     jump to given address and return to CP/M
EX      xxxx     jump to given address and return to CP/POWER
LOAD    fn xxxx  load file to address
SAVE    fn xxxx  save  file from address (optional length 128 byte sectors)
READ    trc sec  read T(rack) S(sector) to 80H (optional addr & sectors)
WRITE   trc sec  write (opposite of READ)
READGR	gr       read group # (optional address & sectors)
WRITEGR	gr       write group # (opposite READGR)
GO      fn xxxx  load file to address and jump to it
SETDIR           set file to $DIR
SETSYS           set file to $SYS
SETRO            set file to $R/O
SETWR            set file to $R/W
DS    xxxx           enter the monitor mode (.Hex .Dec .Ascii .Binary)
DUMP  xxxx yyyy      dump (type) memory
DUMPX xxxx yyyy      dump memory in hex and ascii
DUMPH xxxx yyyy      dump memory in hex
DUMPA xxxx yyyy      dump memory in ascii
FILL  xxxx yyyy n    fill memory
CM    xxxx yyyy zzzz compare memory xxxx to yyyy with zzzz
MOVE  xxxx yyyy zzzz move memory from xxxx-yyyy to zzzz
SEARCH xxxx yyyy a b search memory (ascii=use "xyz", wild cards O.K.)
USR1                 user subroutine #1
USR2                 user subroutine #2
USR3                 user subroutine #3
USR4                 user subroutine #4
RESET                reset drive   (not complete/working)


0100-0102......JMP start of PGM					(C3 xxxx)
0103-0104......not used in CP/M, reserved for MP/M		(00 00)
0105...........paging for directory (current=0=no paging)	(00)
0106...........character used in TYPEx to skip to next file	(0B - ^K)
0107...........POWER's prompt					(3D - =)
0108...........leading character in DS for change of command	(2E - .)
0109...........character used to reverse DS			(7E - ~)
010A...........bad blocks file name consists of this character	(3D - =)
010B...........cancel						(1B - ESCAPE)
010C...........FF=print disk+memory info in direct read/write	(00)
010D...........FF=do not allow BDOS error, stay in POWER	(00)
010E...........0=standard dir, 1=show as CP format (no numbers)	(00)
               FF=show as POWER format with numbers
010F...........stop display (in addition to  ctr/S)		(20 - sp)
0110-0111......end of PGM (-1 = stack)				(?? ??)
0112-0113......input buffer address				(?? ??)
0114...........top of TPA (if 00 00 then use BASE+1)		(00 00)
0116...........0=normal operation, FF=force no buffering	(00)
	       1=force CTR/C
0117...........restart (CF=1,D7=2,DF=3,E7=4,EF=5,F7=6,FF=7)	(00)
0118...........FF=CRT 64, 0=CRT 80, 1=CRT 40			(00)
0119...........sectors to write w/o pre-read in WRITE		(00)
011A...........COPY or LOAD	00=stop if bad sector		(01)
				01=stop and ask if cont
				FF=do not stop if bad
011B...........TEST, COPY or LOAD fill bad block with byte	(E5)
011C...........show user 0 next to prompt if 0FFH (true)	(00)
011D...........input buffer length				(7F)
011E...........0 print sing-on on BOOT & CTR/C			(00)
	       1 print sing-on on BOOT only
	      FF do not print sing-on
011F...........if paging on, stop if this char (0AH or 0DH)	(0A)
	       if 0AH (line feed) the cursor will be at left
	       side of screen over a char; if 0DH (return)
	       then cursor after last char of line.
0120-013F......density reset on ^C (for N* set 0110=00)		(C9 .....)
0140-0147......USR1 routine (current=0C9H=RET)			(C9 .....)
0148-014F......USR2 (sample jumps to CP with sing on/relog)	(C3 xx xx ..)
0150-0157......USR3 (sample jumps to CP with sing on)		(C3 xx xx ..)
0158-015F......USR4 (sample jumps to CP with no sing on)	(C3 xx xx ..)
0160-026F......COMMANDS end commands with 20H 00H		(......20 00)
0170-0172......jump to KEYSTAT (see manual)			(C3 xx xx)
0173-0175......jump to CINPT   (see manual)			(C3 xx xx)
0176-0178......jump to PRINCHA (see manual)			(C3 xx xx)
0179-017B......jump to INBUFER (see manual)			(C3 xx xx)
017C-017F......not used, reserved				(00 00 00 00)